## Slide 1
COMPUTER NETWORKS / REVIEW 1
Graph Neural Network-Driven
Predictive Carbon-Aware Routing
A controlled study of route choices under stale traffic information
Ashutosh Gupta · Tanay Mohta · Avaneesh Chavan
21 October 2026
Notes: Opening: A router can choose a short path, a cleaner-grid path, or a path with spare capacity. The best choice changes as demand changes. We study that choice in a controlled replay.
Team: Ashutosh Gupta 24BCE2983, Tanay Mohta 24BDS0294, Avaneesh Chavan 24BKT0155.
This is Review 1. Describe results as exploratory, not final publication claims.

## Slide 2
THE PROBLEM
A greener route can become the congested route
CARBONROUTE / REVIEW 1
02
At each 15-minute decision point, a network must choose a path for each source–destination flow.
Carbon intensity changes by location
A path through a region with a dirtier electricity mix receives a higher carbon-oriented score.
Traffic information can arrive late
With one-bin telemetry lag, the controller plans using traffic measurements from 15 minutes earlier.
Research question
Can advance demand estimates improve the carbon / congestion trade-off?
Notes: Define a flow as aggregated traffic between an origin and destination. The flow is routed over a sequence of network links.
Carbon intensity is grams of CO2 associated with one kilowatt-hour of grid electricity in a country; our score uses it as a routing proxy.
The 15-minute lag is an experimental condition, not a claim about all real SDN controllers.

## Slide 3
EXISTING WORK
Our question sits between three research lines
CARBONROUTE / REVIEW 1
03
SDN traffic engineering
B4 showed that central control can allocate wide-area network capacity.
Capacity is the primary objective.
Carbon-aware routing
CIRo studies carbon-aware inter-domain routing and even predicts carbon intensity.
Demand-aware congestion safeguards remain a separate question.
Graph learning for networks
RouteNet uses graph neural networks to model network behavior.
A forecast alone does not specify safe route decisions.
Notes: Avoid claiming that every previous carbon-aware approach is reactive. CIRo explicitly uses carbon forecasting.
Our scoped contribution is to combine traffic-demand prediction, carbon-oriented path choice, and conservative capacity safeguards in one reproducible replay, and compare distinct planners.
Sources: B4 https://research.google.com/pubs/archive/41761.pdf ; CIRo https://netsec.ethz.ch/publications/papers/green_routing2023.pdf ; RouteNet https://arxiv.org/abs/1910.01508

## Slide 4
TESTBED
A small, repeatable slice of the GÉANT network
CARBONROUTE / REVIEW 1
04
8
routers in the selected European topology
11
physical links in the subgraph
6
directed origin–destination flows
Traffic replay
SNDlib GÉANT measurements from 2005, sampled every 15 minutes.
Grid signal
Public ECON-PowerCI country data from 2022–24, one value per day.
Dates are matched by season and weekday for a counterfactual replay. The 2005 network did not operate on the 2022–24 grid.
Notes: Explain GÉANT as a pan-European research backbone topology. We use an induced 8-node, 11-link subset to keep routing and training feasible on student hardware.
The 2005 traffic and 2022–24 carbon series are not simultaneous. We align them by weekday and season as a what-if experiment. Within each simulated day, the carbon value stays constant.
Sources: https://sndlib.put.poznan.pl/home.action and https://zenodo.org/records/15987717 . Project methods: docs/PAPER_DRAFT.md and data manifests.

## Slide 5
METHODOLOGY
A forecast informs each 15-minute route decision
CARBONROUTE / REVIEW 1
05
01
Observe
Past OD traffic and the current daily country carbon signal
02
Forecast
Estimate demand 15, 30 and 45 minutes ahead
03
Plan
Reserve link capacity and select one path for each OD flow
04
Replay
Reveal actual trace demand; record overload, service and carbon score
SDN means software-defined networking: one controller computes routes from a network-wide view.
Notes: OD means origin–destination. A single OD demand is the amount of aggregate traffic from one node to another during a 15-minute bin.
We implemented a trace-driven aggregate-flow simulator. No live OpenFlow controller, Mininet packet timing, or observed real emissions appear in the current result.
The model is trained before the replay. It does not learn during the live dashboard demonstration.

## Slide 6
MACHINE LEARNING
The model predicts demand; guardrails handle its errors
CARBONROUTE / REVIEW 1
06
GCN
shares information across connected routers
GRU
learns patterns across successive 15-minute observations
The decision layer uses three safeguards
90th-percentile forecast-error margin
Shared capacity reserved across three horizons
80% planning utilization; 5% improvement and 30-minute hold to limit route flaps
Notes: GCN = graph convolutional network. It lets each node combine features from linked neighboring nodes. GRU = gated recurrent unit, a recurrent model for time patterns.
The model predicts traffic only, not carbon intensity. Carbon uses a fixed daily public grid signal.
The margin comes from validation residuals, not the test set. Hysteresis means we avoid changing a route for a tiny predicted benefit and hold it for two bins, except when predicted risk demands action.
Project source: docs/PAPER_DRAFT.md and router implementation.

## Slide 7
ROUTING METHODS
We test two ways to turn forecasts into paths
CARBONROUTE / REVIEW 1
07
Greedy guarded planner
Chooses one OD flow at a time. Each selection reserves capacity before the next flow is routed.
Priority: reduce predicted overload with conservative headroom.
Joint carbon-budget planner
Tests all 64 combinations of two eligible paths for six OD flows, then chooses a whole-network assignment.
Constraint: predicted carbon score stays at or below the reactive reference; objective: lowest worst predicted link utilization.
Notes: The joint selector is the second branch. It searches 2^6 = 64 assignments. It uses a zero carbon budget fraction relative to reactive routing in the shown comparison.
A predicted carbon budget is a planning constraint. It does not guarantee a lower realized forwarding score in every replay.
Both methods use the same forecast and safety mechanisms. The joint method is an exploratory alternate selector, not a proven replacement for greedy routing.
Source: docs/JOINT_SELECTOR.md and docs/PAPER_DRAFT.md.

## Slide 8
EVALUATION DESIGN
We compare with four routing baselines
CARBONROUTE / REVIEW 1
08
Shortest path
Choose the least-delay route.
Reactive carbon
Use the observed carbon signal and current or delayed traffic.
Predictive traffic engineering
Forecast demand, but do not favor lower-carbon routes.
Persistence + safeguards
Assume traffic stays at its latest value; use the same guardrails.
Compare: forwarding score ↓ overload minutes ↓ served fraction ↑ route changes ↓
Forwarding score measures byte-weighted exposure to regional grid intensity; it is a proxy, not emitted CO₂.
Notes: The forecasting comparison uses five neural training seeds, 42–46. The full evaluation includes 2,475 simulation runs, but they reuse five adjacent test traffic days; the number of independent days is five.
Workloads include normal, bursty and congested traffic, with zero- and one-bin observation delay. The main figures on following slides use congested traffic and one-bin lag.
Forwarding score is a byte-weighted path exposure to country carbon intensities, expressed numerically in g CO2/kWh. It is not measured grams of CO2 emitted.
Source: results/multiseed/summary_multiseed.csv and docs/PAPER_DRAFT.md.

## Slide 9
RESULT A
Joint planning lowers the carbon score in this replay
CARBONROUTE / REVIEW 1
09
Congested demand, 15-minute telemetry lag; one trained seed; five previously inspected test days
ROUTING POLICY
FORWARDING SCORE ↓
OVERLOAD ↓
Reactive carbon
323.83
126 min/day
Greedy GNN
333.18
114 min/day
Joint GNN
303.45
126 min/day
Joint beats reactive on the score by 20.38, with no overload reduction. Greedy relieves overload but increases the score.
Notes: This is an exploratory same-test comparison. Five test days were already inspected during development, so avoid saying it is a fresh holdout or statistically confirmed advantage.
Joint versus reactive score: 303.45 versus 323.83, difference 20.38, about 6.3% lower. Both show 126 overload minutes/day. Greedy GNN is 333.18 and 114 minutes/day in this single-seed joint comparison.
The carbon score is a comparative proxy, not actual electricity use or CO2 mass.
Source: docs/JOINT_SELECTOR.md and results/joint-test-exploratory-final/.

## Slide 10
FRIEND’S PR
Five-seed replication makes the greedy result more credible
CARBONROUTE / REVIEW 1
10
Congested demand + one-bin telemetry lag
126
reactive overload minutes/day
114
greedy GNN overload minutes/day
114
persistence + same safeguards
Observed mean improvement: 12 minutes/day
Day-level paired test: p = 0.099 across five adjacent traffic days. The 2,475 runs do not create 2,475 independent days.
Notes: The updated PR retrains five neural seeds and runs 495 simulations per seed, 2,475 total. It also includes day-clustered tests and a parameter sweep. These are evaluation additions; they do not introduce the joint routing algorithm.
Paired day differences in overload are -15, 0, -15, -30, 0 minutes/day. The paired t-test p-value is 0.099; Wilcoxon p=0.25. Claim an observed replay improvement, not statistical proof.
GNN score 334.75 versus reactive 323.83; persistence 338.58. Both GNN and persistence achieve 114 overload minutes/day. Route changes: 18.68 GNN versus 23 persistence.
Source: PR https://github.com/Tanay-M/CN_Project/pull/1 ; results/multiseed/summary_multiseed.csv ; results/multiseed/statistical_tests.csv.

## Slide 11
MODEL CHECK
The graph model does not win the forecast contest
CARBONROUTE / REVIEW 1
11
Mean absolute demand error across the three horizons, Mbps ↓
Matched GRU
0.4816
Persistence
0.4858
GCN–GRU
0.4948
Interpretation: simple time-series baselines remain strong on this small WAN slice. Route safeguards, rather than a lower GNN forecast error, explain much of the overload result.
Notes: MAE means mean absolute error: the average absolute distance between forecast demand and actual demand. Lower is better.
Matched GRU keeps the temporal model but removes graph mixing. Persistence simply predicts that the latest observed demand will continue.
Five-seed mean MAE: GCN-GRU 0.4948 Mbps; matched GRU 0.4816; persistence 0.4858. Do not claim that the GNN forecasts best.
The numerical differences are small. Source: results/multiseed/forecast_multiseed_summary.csv and docs/PAPER_DRAFT.md.

## Slide 12
FRIEND’S PR
Route stability responds to the planner settings
CARBONROUTE / REVIEW 1
12
Exploratory sweep: 196 configurations / runs on one already-inspected test day
SAFETY MARGIN α
HYSTERESIS τ
ROUTE CHANGES / DAY
0.80
0.00
20
0.80
0.20
13
0.99
0.20
6
All three settings show 60 overload minutes/day in that one-day congested, lagged slice. Stronger dampening raises the carbon-oriented score.
Notes: Alpha is the safety-margin quantile, and tau is the minimum predicted improvement required to switch routes. More conservative values can reduce route changes but may worsen the carbon-oriented score.
This sweep spans seven alpha values, seven tau values, two scenarios and two observation delays, making 196 runs. The displayed rows all use one day, carbon year 2022, congested demand and one-bin lag.
Scores for displayed rows: alpha .80/tau .00 = 516.43; .80/.20 = 523.58; .99/.20 = 543.79. Overload 60 min/day in each. This is parameter exploration, not independent validation.
Source: results/sensitivity/summary.csv and PR #1.

## Slide 13
INTERPRETATION
What the evidence supports today
CARBONROUTE / REVIEW 1
13
Observed trade-off
Joint routing improves the comparative carbon score; guarded greedy routing reduces overload in the lagged congested replay.
A negative ML finding
The GCN–GRU does not beat GRU or persistence in mean demand forecast error on this small topology.
The limits of this evidence
The traffic days are few and reused; 2005 traffic is paired with later grid data; the simulator does not measure packet latency or actual CO₂.
Notes: This honesty is useful in a research review. We are presenting a method, a controlled replay, trade-offs, and limits rather than a universal performance claim.
The score is byte-weighted sender-country carbon intensity accumulated along hops. It cannot be read as kilograms of physical emissions saved.
The aggregate-flow model uses progressive filling. It does not emulate queues, TCP dynamics, or Mininet/OpenFlow switch behavior. Do not claim lower latency from the present measurements.
Five adjacent days create limited statistical power. Sensitivity values are from one previously inspected day.

## Slide 14
LIVE DEMONSTRATION
Use the dashboard to show one decision unfolding
CARBONROUTE / REVIEW 1
14
1
Choose congested traffic and 15-minute observation lag.
2
Compare reactive carbon with joint budget GNN: score falls, overload stays level.
3
Switch to greedy GNN: overload falls, score rises. Scrub time to inspect a link and route.
Open: docs/reports/joint-validation.html
Notes: Before presenting, open the local self-contained dashboard file and test that it loads without a server. The file is docs/reports/joint-validation.html in the main project checkout.
The dashboard displays the joint-validation replay, not the PR multiseed and sensitivity results. Use slides 10–12 for those PR findings.
Demonstration script: select congested workload and lag=1; show reactive versus joint in the comparison values; then choose greedy and describe the trade-off; use the time control to point at a route and utilization change. Avoid claiming live physical network operation.

## Slide 15
CLOSE
Our contribution is a reproducible comparison of routing choices
CARBONROUTE / REVIEW 1
15
Built
A trace-driven GÉANT replay with trained demand prediction, safeguards, two carbon-aware planners, four baselines, and a dashboard.
Learned
The best route depends on the objective. The GNN is not the forecast winner; safety policies and joint selection drive different trade-offs.
Next
Freeze settings, evaluate more independent traffic days, and test packet-level behavior before stronger paper claims.
Notes: End with the main research lesson: a routing system must be judged on its complete decision policy and evaluation protocol, not just model accuracy.
Review 1 asks for work and method. The next two weeks can expand independent traffic windows, verify statistical claims, and optionally add Mininet packet-level validation if feasible.
The current contribution is a controlled simulator and evidence. A paper should avoid saying observed score changes prove real emissions saved.

## Slide 16
SOURCES
Data and research sources
CARBONROUTE / REVIEW 1
16
SNDlib GÉANT topology / traffic: sndlib.put.poznan.pl
ECON-PowerCI grid intensity dataset: zenodo.org/records/15987717
B4 software-defined WAN traffic engineering: research.google.com/pubs/archive/41761.pdf
CIRo carbon-aware inter-domain routing: netsec.ethz.ch/publications/papers/green_routing2023.pdf
RouteNet graph learning for networks: arxiv.org/abs/1910.01508
Project evidence: docs/PAPER_DRAFT.md, docs/JOINT_SELECTOR.md, results/multiseed/, results/sensitivity/
Notes: Project repository: https://github.com/Tanay-M/CN_Project . Friend PR: https://github.com/Tanay-M/CN_Project/pull/1 .
The presentation reflects files and saved results reviewed on 20 October 2026. PR changes were included as exploratory evidence; this deck does not imply the PR has been merged.
SNDlib: https://sndlib.put.poznan.pl/home.action ; ECON-PowerCI: https://zenodo.org/records/15987717 ; B4: https://research.google.com/pubs/archive/41761.pdf ; CIRo: https://netsec.ethz.ch/publications/papers/green_routing2023.pdf ; RouteNet: https://arxiv.org/abs/1910.01508 .